Standard PolyDrain – VectorDrain®

Pre-fabricated Slot Drain 4" ID

Standard Specification

System ID#: 2305 VectorDrain

Trench drain shall be VectorDrain; manufactured by ABT, Inc., 259 Murdock Road, Troutman, NC - (800) 438-6057. www.abtdrains.com

System Components:

Pre-fabricated Slot Drain - System of 78.38” (2m) long and 39.19” (1m) long slot drain channels of polymer concrete and 4 inch ID schedule 40 PVC pipe, in-line polymer concrete catch basins, and accessories. Slot width shall not exceed 1/4” (0.25”) in compliance with Heelproof and ADA requirements.  Over all unit depth is 5.93” (150mm).

Coupler: Sections shall be coupled together with PVC Slip coupler, 3.73” minimum.

Catch Basin: #2900VEC fabricated of polymer concrete.

a. Width:  6" (150mm) OD, 4" (100mm) ID

b. Depth:  22.1" (

c. Length: 19.7” (1/2 m)

d. Cover: polymer concrete, 15/32” (12mm) slot, removable.

e. Locking device for cover.

Quality Assurance:

Submittals:  A Certificate of Compliance in conformance with the provisions of these Standard Specifications shall be furnished to the Engineer.